## Slide 1
Latency test Setup
02
Latency Definition
Time from sending a request until the response is received.
Client device
Mobile phone
Generated sensor-like data
Edge server
Ubuntu laptop
Processed the request locally
Cloud target
Internet server
External online server
Request sent
Response received
Measured latency
Tested in two environments: Paderborn home Wi-Fi (stable, private) · HSHL central Wi-Fi (shared, congested)
Notes: Explain that latency means the full round-trip time. The test used a mobile phone as the client, a laptop as the local edge server, and an external internet server for cloud comparison.

## Slide 2
Edge Latency Test
03
Mobile
phone client
Home or HSHL
Wi‑Fi network
Ubuntu laptop
Flask server
Response
back to phone
Stable local network
95 ms
Paderborn home Wi‑Fi
Shared network
422 ms
HSHL central Wi‑Fi
Test Procedure
Server: Ubuntu 22.04 running Python Flask
Client:
Mobile phone → http://192.168.178.78:5000
Terminal log:
POST /process HTTP/1.1" 200
192.168.178.117 → .78:5000
Status 200 OK confirms successful edge communication.
Notes: Say that in the edge test, the laptop acts like a small local server. The phone sends data over the same Wi-Fi network, the laptop processes it, and the response comes back without going to a remote cloud server.

## Slide 3
Cloud Latency Test
04
Mobile
phone
Internet
route
Remote cloud
server
Response
returns
curl -w "Total time: %{time_total} seconds"
https://httpbin.org/get
Measured cloud latency
510 ms
Worst shared network result
2170 ms
HSHL central Wi‑Fi
Test Procedure
Method: HTTP request via public internet
Target:
https://httpbin.org/get
Command:
curl -w "%{time_total}s"
https://httpbin.org/get
Result: 0.510079 s = 510 ms internet round-trip.
Paderborn home Wi‑Fi
Internet
route
Notes: Explain that the cloud test used a remote HTTP server. The request must go through the public internet, reach the server, and return. This adds round-trip delay.

## Slide 4
Measured Results: Edge vs Cloud
05
Chart: 
| Home Wi‑Fi | HSHL central Wi‑Fi
Edge computing | 95 | 422
Cloud computing | 510 | 2170
Latency in milliseconds (lower is better)
Home Wi‑Fi
95 vs 510 ms
Cloud took about 5.4× longer
HSHL Wi‑Fi
422 vs 2170 ms
Cloud took about 5.1× longer
Notes: Use the chart to show the numbers. At home, edge latency was 95 ms and cloud was 510 ms. At HSHL, edge was 422 ms and cloud was 2170 ms. The direction is the same: edge is lower.

## Slide 5
Latency Formulation
08
C = X / L + D / R
C = latency
X = distance • L = bandwidth • D = data rate • R = computing resources
Edge path
short X
Cloud path
large internet X
What increases delay?
Edge reduces the distance X because processing is local.
A shared network lowers available bandwidth L.
Cloud routes are longer, so strict millisecond response is harder.
Notes: This slide explains the equation in easy words. Edge reduces X because data travels a short local distance. Shared Wi-Fi reduces effective bandwidth, so latency rises. Cloud has a much longer internet route.

## Slide 6
Edge vs. Cloud: Full Comparison
Criterion | Edge Computing | Cloud Computing
Latency (stable network) | 95 ms | 510 ms
Latency (shared network) | 422 ms | 2,170 ms
Speed advantage | 5.1× – 5.4× faster in every test | 
Offline operation | ✓ Yes | ✗ No
Suitable for real-time | ✓ Yes | Limited
Network dependency | Local network | Internet required
Storage & analysis scale | Limited | ✓ High
Edge is best for fast local actions. Cloud is best for heavy storage, training, reporting, and long-term analytics.
Notes: Table III from the paper summarises all key dimensions. Notice that storage and analysis scale is the ONE area where cloud wins. This is why the paper recommends a hybrid approach: edge handles all time-sensitive operations, cloud handles everything that doesn't require an immediate response (storage, analytics, AI model retraining).