## Slide 1
EDGE COMPUTING
in Industrial Communication
Processing data at the source — faster, smarter, more resilient.
Barua · Rahman · Kapil · Chowdhury | Electronic Engineering · HSHL Lippstadt
Notes: Title slide — introduce the paper and the team.

## Slide 2
Agenda
01
Introduction
What is edge computing & why it matters
02
Architecture
Four-layer model: Cloud → Fog → Edge → Devices
03
Benefits
Latency · Bandwidth · Privacy · Reliability
04
Applications
IoT · Automotive · Healthcare · Industry
05
Latency Experiment
Edge vs. Cloud — real measurements
06
Challenges & Conclusion
Limitations and future outlook
Notes: Walk through the six sections of the presentation.

## Slide 3
What is Edge Computing?
1
Closer to the source
Processing happens at local gateways or edge servers — not distant cloud data centers.
2
Three-tier architecture
Field devices at the bottom, edge nodes in the middle, cloud at the top.
3
Millisecond decisions
Factories can't wait: robotic arms, conveyor belts and safety systems need sub-millisecond responses.
4
Resilient by design
Edge systems operate independently even when the cloud connection is lost.
The Problem
Billions of IoT devices generate data that can no longer be efficiently routed to distant cloud servers.
> 500 ms
typical cloud round-trip in industry
Notes: Edge computing moves computation to the network edge — next to factories, hospitals, and vehicles.

## Slide 4
Four-Layer Architecture
Each layer has a defined role — speed-sensitive tasks stay close to the machines.
☁ Cloud Layer
Long-term storage · Model retraining · ERP/MES reporting · Global monitoring
🌫 Fog Layer
Buffer between edge and cloud · Short-term aggregation · Prevents cloud overload
⚡ Edge Layer
Local ML/AI analytics · Protocol translation (MODBUS ↔ OPC-UA) · Anomaly detection
🔌 Field Devices
Sensors · PLCs · Cameras · Robots · IoT modules — raw data sources on the factory floor
Notes: The key insight: latency-sensitive tasks (millisecond control) happen at the edge; long-horizon tasks (analytics, training) happen in the cloud.

## Slide 5
Key Benefits
Low Latency
Processing near the source cuts response times to milliseconds — essential for autonomous vehicles, robotics, and emergency healthcare.
Reduced Bandwidth
Only key results (alarms, status updates) travel to the cloud. Raw data stays local, saving network capacity.
Improved Privacy
Sensitive data (e.g. patient records) stays on-premise. Only necessary summaries reach the cloud.
Better Reliability
Edge systems continue operating when cloud connectivity is poor or lost — critical for remote factories.
Notes: These four benefits make edge computing indispensable for industrial real-time systems.

## Slide 6
Cloud vs. Edge Computing
Cloud Computing
Edge Computing
Processing Location
Central cloud servers
Near the device/user
Latency
High (≥ 500 ms)
Low (< 100 ms local)
Bandwidth Use
High — all data to cloud
Low — only summaries sent
Storage Capacity
Very high (unlimited)
Limited (local storage)
Reliability
Requires internet connection
Works offline
Best Use Case
Big data · ML training · ERP
Real-time control · Safety
Notes: Edge and cloud are complementary, not competing. The hybrid model uses each for what it does best.

## Slide 7
Application Areas
Internet of Things
Smart homes, factories & agriculture process sensor data locally for instant reactions.
Autonomous Vehicles
Cameras and LIDAR data processed on-vehicle — cloud round-trips are too slow for safety.
Healthcare
Wearables and patient monitors trigger local emergency alerts within milliseconds.
Industrial Automation
Fault detection, quality control, and real-time machine monitoring on the factory floor.
Smart Cities
Traffic sensors and cameras analysed locally to reduce congestion and improve safety.
Key Insight
In every domain, the unifying theme is the same: decisions that matter happen in real time, and real time means milliseconds — not the 500 ms+ of a cloud round-trip.
Edge computing bridges the gap between raw sensor data and timely, local intelligence.
Notes: Edge computing is now deployed across virtually every sector where timely local decisions matter.

## Slide 8
Latency Experiment
A real measurement — not an estimate — using two common network environments.
⚡ Edge Computing Test
Mobile Phone → Home Wi-Fi → Ubuntu Laptop (Flask) → Mobile Phone
Python Flask server at 192.168.178.78:5000
Local round-trip measured end-to-end
☁ Cloud Computing Test
Mobile Phone → Internet → Remote Cloud Server → Mobile Phone
curl -w "%{time_total}" https://httpbin.org/get
Internet round-trip measured end-to-end
Two Network Environments
🏠 Paderborn Home Wi-Fi
Private, stable, low contention — closest to ideal industrial private network
🏫 HSHL Central Wi-Fi (Lippstadt)
Shared university network — simulates a busy factory floor environment
Notes: The experiment used a Flask server on an Ubuntu 22.04 laptop as the edge node and httpbin.org as the cloud endpoint.

## Slide 9
Experimental Results
Chart: Latency (ms)
| Paderborn Home Wi-Fi | HSHL Central Wi-Fi
Edge Computing | 95 | 422
Cloud Computing | 510 | 2170
5.4×
faster (home Wi-Fi)
95 ms vs 510 ms
5.1×
faster (HSHL Wi-Fi)
422 ms vs 2170 ms
💡 Key Takeaway
Edge is faster even on congested networks — the gap only widens under load.
Notes: At home, edge is 5.4× faster; under HSHL shared WiFi, edge is still 5.1× faster than cloud.

## Slide 10
Industrial Use Cases
🔩
PCB & SMT Assembly
Camera inspection detects misplaced components, missing solder, or bad orientation. The edge system rejects the board instantly — before bad units continue down the line.
⚙️
CNC Machining
Vibration, temperature, and current sensors feed into an edge node that predicts tool wear before breakage, alerting operators to swap tools proactively.
🤖
Automotive Welding
Each weld's current, voltage, and timing are compared against quality limits in real time. Defective welds are flagged and the robot halted within milliseconds.
💊
Pharma Filling Lines
Cameras check fill level, weight, label position, and packaging integrity. Under-filled or contaminated units are removed before final packaging.
Notes: Cloud-only processing cannot handle any of these scenarios — latency is simply too high for real-time safety decisions.

## Slide 11
Challenges & Limitations
Security Risks
Edge devices are distributed across many sites, making centralised protection difficult. A compromised device can impact the whole system.
Limited Resources
Edge hardware has less compute, memory, and storage than cloud servers. Applications must be carefully optimised.
Management Complexity
Coordinating software updates, monitoring, and fault detection across hundreds of edge nodes is a significant operational challenge.
Data Consistency
Processing data at multiple sites makes it harder to maintain a single consistent view between edge and cloud systems.
Notes: These challenges are real but solvable — dedicated private networks, hardware security modules, and centralised device management platforms address most of them.

## Slide 12
Conclusion
Edge computing is a key technology for modern distributed systems — not a replacement for the cloud, but a complement.
The edge handles latency-sensitive local tasks (fault detection, safety response, quality control).
The cloud handles large-scale storage, model training, and long-term analytics.
Experimental results confirm edge processing is 5.1–5.4× faster across all network conditions tested.
A hybrid edge–cloud architecture is the practical solution for Industry 4.0.
Thank you · Questions welcome
Barua · Rahman · Kapil · Chowdhury | HSHL Lippstadt | Electronic Engineering
Notes: Wrap up: edge + cloud is complementary. Key stat: 5.1–5.4× speed advantage confirmed in real measurements.