## Slide 1
Edge Computing in Industrial Communication
TEAM-A5
Md Mostafizur Rahman
Turja Barua
Deepak Kapil
Moaz Chowdhury
Industrial Communication Standard

## Slide 2
What is Edge Computing?
1
Closer to the source
Processing happens at local gateways or edge servers — not distant cloud data centers.
2
Three-tier architecture
Field devices at the bottom, edge nodes in the middle, cloud at the top.
3
Millisecond decisions
Factories can't wait: robotic arms, conveyor belts and safety systems need sub-millisecond responses.
4
Resilient by design
Edge systems operate independently even when the cloud connection is lost.
The Problem
Notes: Edge computing moves computation to the network edge — next to factories, hospitals, and vehicles.

## Slide 3
Architecture of Edge Computing
Cloud layer
Long-term storage, dashboards, model training, ERP/MES reporting
Fog layer
Buffers and aggregates data between edge and cloud
Edge layer
Local processing, AI/fault detection, protocol translation
Edge devices
Sensors, cameras, PLCs, robots and IoT modules
Notes: Explain each layer from bottom to top: devices create data, edge reacts quickly, fog helps aggregate, cloud stores and analyses for the long term.

## Slide 4
Cloud vs. Edge Computing
Cloud Computing
Edge Computing
Processing Location
Central cloud servers
Near the device/user
Latency
Higher
Lower
Bandwidth Use
High — all data to cloud
Low — only summaries sent
Storage Capacity
Very high (unlimited)
Limited (local storage)
Reliability
Requires internet connection
Works offline
Best Use Case
Big data · ML training · ERP
Real-time control · Safety
Notes: Edge and cloud are complementary, not competing. The hybrid model uses each for what it does best.

## Slide 5
Latency test Setup
02
Latency Definition
Time from sending a request until the response is received.
Client device
Mobile phone
Generated sensor-like data
Edge server
Ubuntu laptop
Processed the request locally
Cloud target
Internet server
External online server
Request sent
Response received
Measured latency
Tested in two environments: Paderborn home Wi-Fi (stable, private) · HSHL central Wi-Fi (shared, congested)
Notes: Explain that latency means the full round-trip time. The test used a mobile phone as the client, a laptop as the local edge server, and an external internet server for cloud comparison.

## Slide 6
Only “HSHL” Wifi USER
03
Notes: Say that in the edge test, the laptop acts like a small local server. The phone sends data over the same Wi-Fi network, the laptop processes it, and the response comes back without going to a remote cloud server.

## Slide 7
Edge Latency Test
03
Stable local network
95 ms
Paderborn home Wi‑Fi
Shared network
422 ms
HSHL central Wi‑Fi
Test Procedure
Server: Ubuntu 22.04 running Python Flask
Client:
Mobile phone → http://192.168.178.78:5000
Terminal log:
POST /process HTTP/1.1" 200
192.168.178.117 → .78:5000
Status 200 OK confirms successful edge communication.
Notes: Say that in the edge test, the laptop acts like a small local server. The phone sends data over the same Wi-Fi network, the laptop processes it, and the response comes back without going to a remote cloud server.

## Slide 8
Cloud Latency Test
04
curl -w "Total time: %{time_total} seconds"
https://httpbin.org/get
Measured cloud latency
510 ms
Worst shared network result
2170 ms
HSHL central Wi‑Fi
Test Procedure
Method: HTTP request via public internet
Target:
https://httpbin.org/get
Command:
curl -w "%{time_total}s"
https://httpbin.org/get
Result: 0.510079 s = 510 ms internet round-trip.
Paderborn home Wi‑Fi
Notes: Explain that the cloud test used a remote HTTP server. The request must go through the public internet, reach the server, and return. This adds round-trip delay.

## Slide 9
Measured Results: Edge vs Cloud
05
Chart: 
| Home Wi‑Fi | HSHL central Wi‑Fi
Edge computing | 95 | 422
Cloud computing | 510 | 2170
Latency in milliseconds (lower is better)
Home Wi‑Fi
95 vs 510 ms
Cloud took about 5.4× longer
HSHL Wi‑Fi
422 vs 2170 ms
Cloud took about 5.1× longer

## Slide 10
Latency Formulation
08
C = X / L + D / R
C = latency
X = distance • L = bandwidth • D = data rate • R = computing resources
Edge path
short X
Cloud path
large internet X
What increases delay?
Edge reduces the distance X because processing is local.
A shared network lowers available bandwidth L.
Cloud routes are longer, so strict millisecond response is harder.

## Slide 11
Edge vs. Cloud: Full Comparison
Criterion | Edge Computing | Cloud Computing
Latency (stable network) | 95 ms | 510 ms
Latency (shared network) | 422 ms | 2,170 ms
Speed advantage | 5.1× – 5.4× faster in every test | 
Offline operation | ✓ Yes | ✗ No
Suitable for real-time | ✓ Yes | Limited
Network dependency | Local network | Internet required
Storage & analysis scale | Limited | ✓ High
Edge is best for fast local actions. Cloud is best for heavy storage, training, reporting, and long-term analytics.

## Slide 12
Industrial Use Cases
🔩
PCB & SMT Assembly
Camera inspection detects misplaced components, missing solder, or bad orientation. The edge system rejects the board instantly — before bad units continue down the line.
⚙️
CNC Machining
Vibration, temperature, and current sensors feed into an edge node that predicts tool wear before breakage, alerting operators to swap tools proactively.
🤖
Automotive Welding
Each weld's current, voltage, and timing are compared against quality limits in real time. Defective welds are flagged and the robot halted within milliseconds.
💊
Pharma Filling Lines
Cameras check fill level, weight, label position, and packaging integrity. Under-filled or contaminated units are removed before final packaging.
Notes: Cloud-only processing cannot handle any of these scenarios — latency is simply too high for real-time safety decisions.

## Slide 13
Key Benefits
Low Latency
Processing near the source cuts response times to milliseconds — essential for autonomous vehicles, robotics, and emergency healthcare.
Reduced Bandwidth
Only key results (alarms, status updates) travel to the cloud. Raw data stays local, saving network capacity.
Improved Privacy
Sensitive data (e.g. patient records) stays on-premise. Only necessary summaries reach the cloud.
Better Reliability
Edge systems continue operating when cloud connectivity is poor or lost — critical for remote factories.
Notes: These four benefits make edge computing indispensable for industrial real-time systems.

## Slide 14
Application Areas
Internet of Things
Smart homes, factories & agriculture process sensor data locally for instant reactions.
Autonomous Vehicles
Cameras and LIDAR data processed on-vehicle — cloud round-trips are too slow for safety.
Healthcare
Wearables and patient monitors trigger local emergency alerts within milliseconds.
Industrial Automation
Fault detection, quality control, and real-time machine monitoring on the factory floor.
Smart Cities
Traffic sensors and cameras analysed locally to reduce congestion and improve safety.
Key Insight
In every domain, the unifying theme is the same: decisions that matter happen in real time, and real time means milliseconds — not the 500 ms+ of a cloud round-trip.
Edge computing bridges the gap between raw sensor data and timely, local intelligence.
Notes: Edge computing is now deployed across virtually every sector where timely local decisions matter.

## Slide 15
Challenges & Limitations
Security Risks
Edge devices are distributed across many sites, making centralised protection difficult. A compromised device can impact the whole system.
Limited Resources
Edge hardware has less compute, memory, and storage than cloud servers. Applications must be carefully optimised.
Management Complexity
Coordinating software updates, monitoring, and fault detection across hundreds of edge nodes is a significant operational challenge.
Data Consistency
Processing data at multiple sites makes it harder to maintain a single consistent view between edge and cloud systems.
Notes: These challenges are real but solvable — dedicated private networks, hardware security modules, and centralised device management platforms address most of them.

## Slide 16
Conclusion
Edge computing is a key technology for modern distributed systems — not a replacement for the cloud, but a complement.
The edge handles latency-sensitive local tasks (fault detection, safety response, quality control).
The cloud handles large-scale storage, model training, and long-term analytics.
Experimental results confirm edge processing is 5.1–5.4× faster across all network conditions tested.
Thank you · Questions welcome
Notes: Wrap up: edge + cloud is complementary. Key stat: 5.1–5.4× speed advantage confirmed in real measurements.